{report:name}
{system:name}

Location: {system:postcode}, {system:city}, {system:country}

Peak Power: {system:performance} kWp
Month: {mdMonth:calc.month}
Report period: {report:timeSpan}

meteocontrol GmbH
Energy & Weather Services
Pröllstraße 28
86157 Augsburg
Germany

# Energy yield
Figure 1. Energy yield of PV plant in the current week. The red bars show the daily energy production.

Table 1. Energy production, specific yield, insolation and availability of the PV plant in the current month.
	Energy production	Spec. yield	Insolation	Plant availability
{START}{mdDay:calc.date}	{mdDay:calc.E_ZAEHLER} kWh	{mdDay:calc.E_N} kWh/kWp	{mdDay:calc.E_GM}{END} Wh/sqm	{mdDay:calc.VFG} %

{mdMonth:calc.month}	{mdMonth:calc.E_ZAEHLER} kWh	{mdMonth:calc.E_N} kWh/kWp	{mdMonth:calc.E_GM} Wh/sqm	{mdMonth:calc.VFG} %

Explanation to 1:
Energy production	Produced energy of the PV plant in kWh, measured at the energy meter.
Specific yield	The energy production normalised to the installed peak power of {system:performance} kWp.
Insolation	Solar irradiance in module plane measured by the on-site installed sensors. If more than one sensor is installed the average of the measurement is calculated. The insolation values between 0 and 4 AM are neglected. / The insolation to the specification in yield reports has to be referenced to pyranometers which are installed in module plane. The difference of the insolation measured by pyranometers and crystalline sensors is typically 3–5 %.
Availability	Availability of the plant in %, calculated in respect to the equations defined in the O&M contract.

Performance Ratio: {mdMonth:calc.PR} %

Comment to the performance ration: The PR equals the quotient of the specific yield and the insolation in module plane. If the insolation is not measured with a pyranometer but with crystalline sensors, one has to take into account that the PR will be overestimated. Furthermore, the monthly PR cannot be compared the annual PR as the PR depends on seasonal fluctuations. An annual performance check is recommended for a analysis of PR and yield.

# Yield prognosis and actual/rated yield comparison
Figure 2. Comparison of rated and actual yield in the current week. The bars show the daily energy production of the plant. The yellow crosses represent the rated yield based on a daily yield calculation taking the plant configuration and the insolation into account. The areas in the background show the ranges for a positive (green), sufficient (yellow) and poor (red) yield.

The actual yields of the PV plant for the current month and current year are opposed to the rated yield values based on simulations of the monitoring portal. The automated simulation takes the plant confuguration (modules, inverters, mounting system) and the measured insolation into account. The automated simulation cannot replace a yield report for the considered time period.
Time period	Actual yield	Rated yield by a simulation
current month ({mdMonth:calc.month})	{mdMonth:calc.E_ZAEHLER} kWh	{mdMonth:sim.E_Z_EVU} kWh
current year ({mdYear:calc.year})	{mdYear:calc.E_ZAEHLER} kWh	{mdYear:sim.E_Z_EVU} kWh

Figure 3. Comparison of the actual yield (red curve) and the rated yield (yellow curve) as well as the yield prognosis of the plant (blue curve) based on a yield report with long-term insulation data.

In the following table the specific actual yield of the plant is compared to the rated yield based on a yield report. The rated yield has been calculated by a yield simulation taking the long-term insolation into account. The real insolation of a considered time period can fluctuate for each operating year.
Month	Specific actual yield	Specific yield of yield report
{START}{ep:month}.{ep:year}	{ep:SpecificYield} kWh/kWp	{ep:YieldForecast} kWh/kWp{END}

# Malfunctions of last month
{START}Ticket-Id	{fp:ticketid}		{fp:begin}	to	{fp:closed}		Status	{fp:status}
Malfunction	{fp:description}					Yield loss:		kWh
Summary	{fp:summary}

								{END}